PRESS ENQUIRIES					                  TRADE ENQUIRIES

| Bryan Richardson | Glenn Taylor |
| --- | --- |
| Richardson Public Relations | ABB Instrumentation Ltd |
| 38 Mayfield Crescent | Howard Road |
| Brighton, E.Sussex BN1 8HQ | St Neots |
|  | CAMBS PE19 3EU |
| Tel: (01273) 506667 | Tel: (01480) 475321 |
| Fax: (01273) 551756 | Fax: (01480) 218361 |
|  | ABB-KT/560 | 11th February, 2000. |

ABB LAUNCHES AQUAPROBE 11

- An Insertion Flowmeter with New Technology Electronics -

The success of ABB’s AquaProbe insertion flowmeter in providing major water companies world-wide with a cost-effective alternative to in-line flow measurement, particularly in locations lacking external power, has led to the launch of AquaProbe 11 - an advanced version offering significantly greater functionality and a three-fold increase in battery life.

The manufacturers, ABB Instrumentation, see this new extension to the AquaProbe range as representing a major step forward for insertion flowmeter capability. The key lies in the incorporation of the high-specification transmitter from ABB’s new technology AquaMaster flowmeter. This not only provides multiple displays for forward/reverse flow rates and totals but also extends to users the opportunity to benefit from the unique AquaMaster concept of integrating high-accuracy flow measurement performance, advanced pressure measurement, data acquisition and radio telemetry capability - all within a single instrument.

Another major improvement for locations where there is no external power is that the transmitter battery will operate continuously for up to three years, whereas that for

More.......

(1)

ABB-KT/560 Continued......

the existing AquaProbe meter is flash powered every 15 minutes and has a life span of only one year. AquaProbe 11 is also available as an a.c.-powered meter with optional battery backup to ensure that there is no loss of flow measurement in the event of power failures.

AquaProbe 11 is a ‘no fuss’ instrument featuring a ‘fit and flow’ facility for fast, error-free installation and can be fitted without disruption to the water supply, thus eliminating the need for major excavations often required for in-line metering. The instrument features a wide flow range with a capability to provide accurate measurements, even at low night flow rates which other insertion flowmeters often fail to register.

Both the probe and transmitter are fully submersible with IP68/NEMA 6P protection rating and the absence of any moving parts results in increased reliability and reduced maintenance. AquaProbe 11 can be used on pipe sizes from 200-2000mm for centreline mounting, and up to 8000mm for critical positioning - the transmitter being mounted either locally or up to 200m (650ft) remote from the probe to facilitate ease of reading.

With the flexibility of a two-in-one flowmeter, AquaProbe 11 can be permanently installed as a monitoring device for economic management of the water supply, or used as a portable site survey tool to check for leaks or to identify hydraulic problems in the existing network. In either application, its high sensitivity enables the instrument to be used to traverse across the pipe to establish the flow profile - a feature for additional management data often overlooked in systems design.

ABB Instrumentation Limited is a major UK operation within the ABB Group’s Automation Business Segment which totals US $9 billion in annual sales, employs 56,000 people throughout the world and has more than 1,000 operating units in 45 countries.

END

(2)