READER ENQUIRIES					       PRESS ENQUIRIES

| Bob Kingman | Bryan Richardson |
| --- | --- |
| ABB Automation Ltd | Richardson Public Relations |
| Howard Road | 38 Mayfield Crescent |
| St Neots | Brighton |
| CAMBS PE19 3EU | East Sussex |
| Tel: (01480) 475321 | BN1 8HQ |
| Fax: (01480) 218361 | Tel: 01273 506667 |
| e-mail: bob.kingman@gb.abb.com | Fax: 01273 551756 |
|  | ABB-KT/577 | 19th July, 2001. |

NEW ABB REMOTE TRANSMITTER SEALS

REDUCE HIGH-TEMPERATURE PROCESSING COSTS

A new development in remote pressure transmitter diaphragm seals which eliminates the need for costly exotic wetted materials when applied to corrosive, high-temperature, high-vacuum processes has been launched by ABB Automation.

The new S6 range of 600T EN Remote Diaphragm Seals from ABB features as standard a tough, corrosion-resistant Teflon PFA film which is hot-deposited on to a stainless steel diaphragm using a unique, glue-free, chemical bonding process. As a result, the seal can cope with most corrosive process media and will give reliable performance in high working temperatures up to 250oC and close to full vacuum working pressures. This compares with maximum working temperatures of between 140oC and 150oC for the majority of standard remote seal coatings available which are usually glued to the metalwork.

Enhancing ABB’s range of 600T EN differential, gauge and absolute pressure transmitters, S6 600T EN remote seals are aimed at processes using highly corrosive media such as those in the chemical, petrochemical and pharmaceutical sectors. They provide the ideal solution for cost-effectively running plants more efficiently at higher

(1)                                                      More....

ABB-KT/577 Continued......

temperatures since, under such conditions, operators no longer need to invest in expensive wetted materials such as Hastelloy C, Titanium, Monel or Nickel.

ABB’s 600T EN pressure transmitters which includes the latest SIL 2 & 3 safety models, feature an MTBF of more than 100 years and are supplied world-wide together with a remote seal portfolio of some 18,000 variants.

END

ABB (www.abb.com) serves customers in manufacturing, process and consumer industries, the utilities and the oil, gas and petrochemicals sector. Over 160,000 people are employed in more than 100 countries.

..................................