# EMC Plan for CE-marked products

This is a form for making an EMC plan where the user and the manufacturer analyze the installation and define the measures to be taken to achieve electromagnetic compatibility. The plan defines the responsibilities of the manufacturer, the installer and the user of the drive. All these parties establish the plan jointly. Fill in and answer the questions below.

| Step 1: Name the parties |
| --- |
| Manufacturer/supplier |  |
| End user |  |
| Order no. |  |
| Type of facility (e.g. chemical factory, paper machine) |  |
| Application (e.g. pump. fan, conveyor) |  |

| Step 2: Collect power distribution and earthing data |
| --- |
| Power Distribution | Point of coupling: identification code for distribution panel, switchgear or transformer |
|  | Type of distribution system | TN-C TN-S TT IT |
| Earth Bus | How and where bonded? |

| Step 3: Collect EMC data (High frequency range, only) |
| --- |
| RFI Sensitive Equipment in the Facility | Any equipment in the building or near installation location sensitive to RF disturbances (e.g. process control and measurement, data buses, computers, remote control, etc.)? Describe. | Yes No |
|  | Approximate distance from PDS and cabling of PDS | .... metres |
|  | Most likely coupling path for disturbance | Conducted Radiated |
| RFI Sensitive Equipment Outside the Facility | Any broadcast or communications receiver antennas visible or near the facility (e.g. radar, radio/TV broadcast, amateur, microwave or other)? Describe. | Yes No |
|  | Frequency | … Hz |
|  | Distances from the antenna | … metres |

| Step 4: Define the installation rules |
| --- |
| Follow the installation rules given in the hardware manual of the drive. Assess the following items and describe the solutions. |
| EMC Effectiveness | Items to Be Considered |
| Cabling | - separation of high-power and low power or signal cables - minimisation of parallel length / segregation distances - cable intersection at 90( - cable positioning in cable trays - earthing of cable trays. |
| Dedicated Transformer | - dedicated isolation transformer - transformer with electrostatic shield. Describe (size, location) |

Signature(s) by person(s) responsible for EMC

Date

Signature(s)