## Slide 1: ABB Robotics-Press Automation
RobotWare StampApp
ABB DMRO Press Automation; Carlos Pastor, Pau Pérez, Ramon Casanelles 2016-06-09

## Slide 2: RobotWare StampApp
The core component of StampPack
RobotWare StampApp is the core value of StampPack, a Stamping Function Package, to facilitate the automation of different variety of Stamping cells.
StampApp provides a friendly environment to integrate, program and operate robotic stamping cells. Its configuration tool brings an unprecedented flexibility for stamping processes.
RobotWare StampApp includes:
  Wizard to facilitate robot programming
  HMI to easily interact with the robot
  Basic pre-engineered interphase to connect robot with cell devices.
  Configurator to edit (if required) production processes.
Differentiated value proposition: Integration, programming and operation of robotic stamping cells made easy!

## Slide 3: RobotWare StampApp
The core component of StampPack
StampPack main components:
Robot
  (IRB 2600 / 4600 most common’s, but could be any other)
RobotWare StampApp
(Option):
  Connection box
  Robot Safety interface
If not included in StampPack, to added by Integrator / End customer
IRC5
IRC5
  Connection box
  Safety interface box

## Slide 4: Main product features StampApp, the application software for Press Cells
Examples of Stamping cells based on StampPack / StampApp:
1 device
2 devices
3 devices
4 devices
5 devices
Press Line

## Slide 5: Reference examples of installations (Non automated)

## Slide 6: Reference examples of automated cells

## Slide 7: StampApp
3 devices layout example: Cell configuration
Conveyor
Robot
Destacker
Press
Defining a cell topology
  Setting up a Robot system with 3 devices through standard Robot Installation Manager
  Assigning names to each cell device
Click for details
Defining no. devices

## Slide 8: StampApp 3 devices layout example: How to program:
Same IO Interface per device
Program Steps:
  Step 1: Part Name and ID
  Step 2: Program Structure
  Step 3: Teaching
Conveyor
Robot
De-stacker
Press

## Slide 9: StampApp Step 1: Part ID and Name
Conveyor
Robot
Destacker
Press

## Slide 10: StampApp Step 2: Program structure definition - Destacker
Conveyor
Robot
De-stacker
Press

## Slide 11: StampApp Step 2: Program structure definition - Press
Conveyor
Robot
De-stacker
Press

## Slide 12: StampApp Step 2: Program structure definition - Conveyor
Conveyor
Robot
De-stacker
Press
Program structure (Step 2)
has been completed

## Slide 13: StampApp Step 3: Programming
Conveyor
Robot
Destacker
Press

## Slide 14: StampApp Step 3: Programming destacking paths and points
Conveyor
Robot
De-stacker
Press
Click for details
Editing default profile

## Slide 15: StampApp Step 3: ModPos, Move type, Speed, zone….
Conveyor
Robot
De-stacker
Press

## Slide 16: StampApp Step 3: Programming press paths and points
Conveyor
Robot
De-stacker
Press

## Slide 17: StampApp Step 3: Programming conveyor path and points
Conveyor
Robot
De-stacker
Press

## Slide 19: StampApp
Defining no. of devices
Back
  Setting up a Robot system with 3 devices through the standard Robot Installation Manager

## Slide 20: StampApp
Editing block profile
Back
Editing default profile, through StampApp Configurator
StampApp Configurator is a web application running on the robot, accessible trough any web browser