| Reference information (e.g. Purchase order no.): |  |
| --- | --- |

RES 521*1.0

Phasor Measurement Terminal

Based on 1MRK 511 115-BEN rev: D

Issued: February 2004

Ordering Guidelines

The analog transformer input modules (type AIM) are configured to the application with a maximum of 6 input transformers for current and 3 input transformers for voltage for each analog input module; a maximum of 2 analog input modules can be included. The basic versions occupy 1/1 of a 6U 19” rack. Totally, 1 rack position is intended for I/O boards in the 1/1 rack. The RES 521 Phasor Measurement Terminal contains hardware always needed as well as the software functions. The hardware in the terminal is fixed, except for the optional second AIM module and the auxiliary dc voltage level of the power supply module.

Product specification

| Ordering Number | 1MRK 002 056-BA | Quantity |  |
| --- | --- | --- | --- |
| Basic data: |
| Nominal frequency: | 50/60 Hz |  |  |  |  |  |
| Rated VT input voltage (across each individual input) | 100/v3, 110/v3, 115/v3, 120/v3, 100, 110, 115, 120 V |
| Rated CT input current | 1/5 A |
| Auxiliary dc voltage EL | 24-60 V or 90-250 V (to be selected below) |  |  |  |  |  |  |

Hardware

In the tables below the hardware requirements for RES 521 have been listed. If the hardware is ordered according to the tables, also the corresponding configuration will be downloaded in the terminal.

| PSM Module Auxiliary dc voltage Available options for Power Supply Module |
| --- |
| 24-60 V |  | 1MRK 002 239-AA |
| 90-250 V |  | 1MRK 002 239-BA |

| AIM Module with standard connection compression screw 7I + 3U ) |
| --- |
| Note:Select the required type of module per slot location. Make sure that the same type of AIM is selected for slots P1 and P5 |
| Analog Input Module 1 (Located in Slot P1) |  |  | 1MRK 001 162-AD |
| Analog Input Module 2 (Located in Slot P5) Optional addition |  |  | 1MRK 001 162-AD |
| AIM Module with ring-lugs screw connection 7I + 3U ) |  |  |  |
| Note:Select the required type of module per slot location. Make sure that the same type of AIM is selected for slots P1 and P5 |
| Analog Input Module 1 (Located in Slot P1) |  |  | 1MRK 001 162-DA |
| Analog Input Module 2 (Located in Slot P5) Optional addition |  |  | 1MRK 001 162-DA |

| IOM Module Available rated voltages for optocouplers Inputs on IOM Module |  |
| --- | --- |
| Rule:One IOM card must be chosen for position 9. Select the rated voltage for optocouplers inputs in the IOM type of module |  |
| 24/30 V dc | 1MRK 000 173-GB |
| 48/60 V dc | 1MRK 000 173-AC |
| 110/125 V dc | 1MRK 000 173-BC |
| 220/250 V dc | 1MRK 000 173-CC |

| Communication PMC |  |
| --- | --- |
| Rear communication via optical fiber on 100 Base Fx Optional addition | 1MRK 002 058-AA |

Mechanical options

| First test switch COMBITEST test switch module RTXP 24 for the first AIM | 1MRK 000 371-EA |
| --- | --- |
| Second test switch COMBITEST test switch module RTXP 24 for the second AIM | 1MRK 000 371-EB |
|  | NOTE! The test switches have internal star point connection of each of the three-phase CT groups per AIM. Each analog input module AIM is connected to its own test switch module so two test switches are needed if two analog input modules are used. Each RTXP 24 test switch module will be mounted in a separate RHGS 6 case with window door. The terminal is reconnectable and can at any time be altered between 1 or 5 A. |
| DC-supply |  |  |
|  | On/Off switch for the dc-supply |  |  |  | RK 795 017-AA |
| Mounting details Mounting details with IP40 degree of protection from the front for the terminal case and if needed the extra test switch cases: |
|  | Phasor Measurement Terminal | One test switch case | Two test switch case |
| 19” rack | 1MRK 000 020-CA | 1MRK 000 020-BE | 1MRK 000 020-BB |
| Wall mounting (applicable for terminal and for test switch) | 1MRK 000 020-DA | 1MRK 000 020-DA | 1MRK 000 020-DA |
| Flush mounting (applicable for terminal and for test switch) | 1MRK 000 020-Y | 1MRK 000 020-Y | 1MRK 000 020-Y |
| Flush mounting with IP54 (Only available for flush mounted terminals) | 1MRC 980 001-2 | 1MRC 980 001-2 | 1MRC 980 001-2 |
| No mounting details |  |  |  |  |
| GPS Antenna |  |  |  |  |  |  |  |  |  |  |
| GPS Antenna |  |  |  | 1MKC 690 002-2 |
| Antenna cable (L=40m) |  |  |  |  | 1MRK 001 665-BA |
| Set of antenna mounting details |  |  |  | 1MRK 001 641-AA |

Manuals

| One CD with all 500 series manuals is always delivered with each terminal |
| --- |
| Rule: Specify the number of extra CD´s requested | Quantity: | 1MRK 002 241-AA |
| Rule: Specify, the number of printed manuals requested |  |  |
| Technical reference manual | Quantity: | 1MRK 511 115-UEN |

Reference Information

| For our reference and statistics we would be pleased if we are provided with the following application data: |
| --- |
| Country: | End user: |
| Substation name: | Voltage level (s): | kV |
| Application: |  |  |

Manufacturer

ABB Automation Technologies AB

Substation Automation

SE-721 59 Västerås

Sweden

Telephone: + 46 (0) 21 34 20 00

Facsimile: + 46 (0) 21 14 69 18

Internet: http://www.abb.com/substationautomation

# Footnotes

) 7I + 3U = Seven CT Inputs ( of which six are used ) and Three VT Inputs

) Ring-lug option does not fully comply with EN 50178