PRESS ENQUIRIES					                 TRADE ENQUIRIES

| Bryan Richardson | Glenn Taylor |
| --- | --- |
| Richardson Public Relations | ABB Instrumentation Ltd |
| 38 Mayfield Crescent | Howard Road |
| Brighton, E.Sussex BN1 8HQ | St Neots |
|  | CAMBS PE19 3EU |
| Tel: (01273) 506667 | Tel: (01480) 475321 |
| Fax: (01273) 551756 | Fax: (01480) 218361 |
|  | ABB-KT/576 | 12th September, 2000 |

ABB RAISES THE STANDARDS FOR

LOW FLOW METERING

‘MagMaster Loflo’ - the latest range of electromagnetic flowmeters developed by ABB Instrumentation for water and wastewater applications - sets new standards for low flow metering capability. Minimal night flows can now be metered with greater precision and those that previously were too low to be detected can now be registered and accurately measured.

The new range which inherits key performance benefits of the world-leading MagMaster pedigree, is expected to have a significant impact on water companies striving to perfect their leakage reduction schemes. MagMaster Loflo can measure minimal flow rates three times lower than is practicable with conventional meters, thus reducing even further the gap through which unaccountable water is invariably lost to leakage. For example, in an average 100mm pipe, MagMaster Loflo provides high-accuracy measurements of minimal flow rates down to 0.041 litres per second while, in the larger 600mm pipe size, measurement reliability down to 2.5 litres per second can be achieved.

(1)                                                  More.....

ABB-KT/576 Continued.......

Available in pipe sizes from 15mm to 600mm (½ to 24 inches), the new range addresses a wide spectrum of water and wastewater applications for measuring bi-directional low flows with self-diagnostics and programmable multiple alarm capability built in as standard. Sensors are both submersible (IP68, NEMA 6P) and buriable, with robust construction that ensures long, maintenance-free life under the arduous conditions associated with the water and wastewater environment.

A remote or integral transmitter offers a choice of display, configuration and communications options, while standard features include forward, reverse and net flow totalisers, flow rate, alarm monitoring and automatic self-diagnostics to ensure integrity. All data and values are in customer-defined units of measurement and there is a choice of current, pulse, serial data and Smart HART communications to assure systems compatibility.

Multi-level password protection guards against inadvertent program or settings changes and data can be stored in non-volatile memory for 10 years retention. In line with all ABB MagMaster flowmeters, the MagMaster Loflo comes with a two-year warranty as standard.

ABB Instrumentation Limited is currently being integrated with ABB’s UK automation company to create a single industrial IT organisation. The new, combined business will trade as ABB Automation Limited, forming a major UK operation within the ABB Group’s Automation Business Segment which totals US $9 billion in annual sales, employs 56,000 people throughout the world and has more than 1,000 operating units in 45 countries.

END

(2)