(PRESS RELEASE)

(Photo Ref:

PRESS ENQUIRIES					    TRADE ENQUIRIES

|  | Tel: | Tel: |
| --- | --- | --- |
| Fax: | Fax: |
|  | ABB-KT/ | Date: |

.

ABB ANALYSERS INTEGRATE

TEMPERATURE OUTPUT

A time and money-saving opportunity for waste-water and industrial effluent treatment plants comes with the introduction by ABB Kent-Taylor of an optional second current output for its 4600 Series of on-line pH, conductivity and dissolved oxygen analysers. This enables users to retransmit both the measured parameter and the sample temperature reading from a single instrument.

The monitoring of effluent temperature - an increasingly important factor in compliance with discharge consent limits - is normally a separate function using dedicated measuring devices. By introducing the second current output to its 4600 analyser series, ABB has utilised data from the instruments’ automatic temperature compensation facility to provide this additional information as an integral part of the analyser’s operation.

The ability to retransmit both temperature and measured parameter conveniently and cost-effectively from a single ABB 4600 Series analyser is just one benefit from the output enhancement. Alternatively, users may retransmit the measured parameter -

More.........

ABB-KT/478 Continued....

‘turbidity’, for example - to two independent locations. Typically, this enables, data to be recorded locally. while, at the same time, being independently transmitted to a main control room.

The ABB 4600 Series of analysers is also available with MODBUS serial communications and four-language software.

END