Technote: technote_100607_Harness IRB 6640

Title: Manipulator harness IRB 6640

Product Type: 	IRB 6640

Year Model: 	M2004

Keywords:	Harness, harness axis 1-6

Author: 	Ulf Back

Revision:-	A

_____________________________________________

Modification of spare parts

- Manipulator harness axis 1-6

Revison 11 or lower of Spare part 3HAC024385-001and 3HAC024386-001 Manipulator harness axis 1-6 on IRB 6640 need to be modified before use on IRB 6640.

Before installation the clamp (3HAC11497- 7, figure 1) for attachment of the harness in the upper part of the lower arm must be exchanged.

Existing clamp 3HAC028615-001 used on the original harness shall be used. See Instruction.

New!

Revision 12 or higher can be used on IRB 6640 without any modification.

Revision 12 was introduced as spare part August, 2010

- Manipulator harness axis 1-4  (IRB 6640ID)

Spare part 3HAC14940-1 and 3HAC16331-1 Manipulator harness axis 1-4 need to be modified before use on IRB 6640ID.

Existing clamp 3HAC028615-001 used on the original harness shall be used.

New!

Spare part 3HAC039428-001 (3HAC14940-1 with new clamp 3HAC038354-001) and spare part 3HAC039429-001 (3HAC16331-1 with new clamp 3HAC038354-001) is recommended.

See technote_081103 Rev B _Manipulator harness IRB 66X0/7600 for further information.

Instruction

- Remove the clamp 3HAC11497-7 from the new harness. Refer to figure 1.

Note! Harness axis 1-6 with clamp 3HAC11497-7 can only be used on IRB 6600/6650/6650S due to L = 20 mm.

- Remove the original clamp 3HAC028615-001 from the replaced harness axis 1-6. Refer to figure 2.

- Install the original clamp on the new harness according to figure 2.

Note! Harness axis 1-6 with clamp 3HAC028615-001 with L=25 mm can only be used on IRB 6640 robots.

- Wrap a Velcro strap, 3HAC12625-1, first around the harness then around the attachment part of the clamp according to figure 3.

- Tighten the strap and make sure that it is closed.

# Text boxes

3HAC028615-001

L= 20

3HAC11497-7

Figure 3

Velcro strap

Attachment part of the clamp

L=25

Figure 2

Figure 1