## Slide 1: AF NEMA contactors
2020 12
The latest technology is our standard

## Slide 2: AF NEMA contactors
Introduction
Speed-up your projects
Optimized logistics
Continuous operation
Contents

## Slide 3: Introduction

## Slide 4: AF NEMA contactor range
The latest technology is our standard
Secure uptime and optimize stock with the latest AF technology for motor starting and power switching up to 1650 A

## Slide 5: 3-Pole range overview
AF09N00 … AF1650N8
Contactors | AF09N00 | AF12N0 | AF26N1 | AF40N2 | AF80N3 | AF140N4 | AF265N5 | AF460N6 | AF750N7 | AF1650N8
NEMA Size | 00 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Rating (hp) 200 V | 0,5 | 3 | 7,5 | 10 | 25 | 40 | 75 | 150 | - | -
Rating (hp) 230 V | 0,5 | 3 | 7,5 | 10 | 30 | 50 | 100 | 200 | 300 | 450
Rating (hp) 460 V | 2 | 5 | 10 | 25 | 50 | 100 | 200 | 400 | 600 | 900
Rating (hp) 575 V | 2 | 5 | 10 | 25 | 50 | 100 | 200 | 400 | 600 | 900
Continuous amp rating (A) | 9 | 18 | 27 | 45 | 90 | 135 | 270 | - | - | -

## Slide 6: AF basic functionality
  Continuous current and voltage coil control trough the entire operating cycle
    Distinct closing sequence
    Low consumption holding sequence
    Monitored opening sequence
  Strong making force
  Low heat dissipation in closed position
  Humming and buzzing free
Optimized DC magnet with electronic control
Coil terminals
Electronic PCB
Contactor coil

## Slide 7: Optimized logistic

## Slide 8: Optimized logistics
Only 4 coils
AF09N00, AF12N0, AF26N1, AF40N2, AF80N3, AF140N4, AF265N5 |  |  | AF460N6, AF750N7, AF1650N8* |  | 
Coils | V AC 50/60 Hz | V DC | Coils | V AC 50/60 Hz | V DC
Code 11 | 24...60 | 20...60 | Code 68 |  | 24...60
Code 12 | 48...130 | 48...130 | Code 69 | 48...130 | 48...130
Code 13 | 100...250 | 100...250 | Code 70 | 100...250 | 100...250
Code 14 | 250...500 | 250...500 | Code 71 | 250...500 | 250...500
* AF1650N8 only available with coil 70 : 100…250 V 50/60Hz, 100…250 V DC |  |  |  |  | 

## Slide 9: Speed-up your projects

## Slide 10: Speed-up your projects
Note about AF NEMA coil interface for PLC
AF460N6
AF1650N8
AF09N00
AF80N3
RA4
Interface relay
AF09N00 up to AF80N3
Built-in PLC interface
AF460N6 up to AF1650N8

## Slide 11: Speed-up your projects
Thermal and electronic overload protection
Thermal O/L | TF42 | TF65 | TF96 | TF140DU | -
Range (A) | 0,10 … 38 A | 22 … 67 A | 40 … 96 A | 66 … 142 A | -
Electronic O/L | EF19 | EF45 | EF65 | EF96 | EF146DU | EF370 | EF460 | EF750 | EF1250DU
Range (A) | 0,10 … 18,9 | 6 … 45 | 20 … 70 | 36 … 100 | 54 … 150 | 115 … 380 | 150 … 500 | 250 … 800 | 375 … 1250
Contactors | AF09N00 | AF12N0 | AF26N1 | AF40N2 | AF80N3 | AF140N4 | AF265N5 | AF460N6 | AF750N7 | AF1650N8
Rating (hp) 200V | 1,5 | 3 | 7,5 | 10 | 25 | 40 | 75 | 150 | - | -
Rating (hp) 230V | 1,5 | 3 | 7,5 | 10 | 25 | 50 | 100 | 200 | 300 | 450
Rating (hp) 460V, 575V | 2 | 5 | 10 | 25 | 50 | 100 | 200 | 400 | 600 | 900
Width (mm) | 45 |  |  | 55 | 70 | 90 | 140 | 190 | 210 | 438

## Slide 12: Thermal overload relays
  TF.. Series based on new technology1
  Trip Class 10
  Operating temp. range -25 up to 60°C
  Manual/ automatic reset selectable
  Test function
  Separate STOP button
  Sealable cover for current setting, reset selection and test function
  Perfect match to the contactor
  Also available: ATEX certified types and kits for separate mounting
Basics TF series
Current setting
Reset button
Stop button
Test/ Status indication
Marking
Cover, sealable

## Slide 13: Electronic overload relays
  Trip Class 10E, 20E, 30E selectable
  Operating temp. range -25 up to 70°C
  Manual/ automatic reset selectable
  Test function
  Separate STOP button
  Sealable cover for current setting, reset selection and test function
  Perfect match to the contactor
  Also available: ATEX certified types and kits for separate mounting
Basics EF series
Current setting
Cover, sealable
Stop
Test/ Status indication
Marking
Trip class selection
Reset

## Slide 14: Continuous operation

## Slide 15: Continuous operation
Coil operating limits
Uc
+10%
-15%
253V
230 V
187 V
IEC 60947-1 requirement
+10%
-15%
230 V
220 V
187 V
253V
Conventional coil
+10%
-15%
250 V
100 V
85 V
275V
AF coil

## Slide 16: Continuous operation
IEC 60947-1 requirement
Conventional coil
AF coil
Drop-out zone
60 V
Safe
!
165 V
Uncertain
!
173 V
Uncertain
+10%
-15%
230 V
220 V
187 V
253V
+10%
-15%
250 V
100 V
85 V
275V
Uc
+10%
-15%
253V
230 V
187 V