(PRESS RELEASE)

(Photo Ref:	1830/97C)

PRESS ENQUIRIES					    TRADE ENQUIRIES

|  | Tel: | Tel: |
| --- | --- | --- |
| Fax: | Fax: |
|  | ABB-KT/ | Date: |

.

FATTY FEEDS PROBLEM SOLVED BY MASSMETER

At the bulk poultry feeds mill of Cymru Country Feeds, Wrexham, an ABB Kent-Taylor K250 MassMeter is providing both the accuracy and the reliability required for dosing essential dietary fats onto poultry pellets, at a mass flow rate of 2500kg/hr.

Mill Manager Mr Andrew Cree reports: “We are very pleased with its performance since its installation in July 1996. The previous flowmeters proved very troublesome, because they had conventional seals and moving parts which were badly attacked by the feedstock (vegetable oils at 60°C - 70°C), with much downtime.”

“The result was growing inaccuracy in the dosing and, as the seals failed, oil and fat leaked and then spread all over the plant. Apart from production losses, it was both hazardous and caused a hygiene problem. The ABB MassMeter has solved all of these problems very satisfactorily.”							Cont......

2....

The K250 MassMeter, teamed with an ABB Kent  Taylor 1210 Transmitter, pumps the vegetable oil at 30 psig to the spray nozzles. The intermittent pumping cycle provides 1,250 kg of oil in 30 minutes to the spray head which feeds the spray cycle over the poultry pellets at the end of the feed production line.

The oils (SG 0.95) are kept warm to maintain their viscosity at around 1050 centipoise, and to improve their absorption rate into the pellets. When the oil is mixed in and absorbed, it is loaded into bulk hoppers for trucking to the broiler poultry farms.

The required accuracy of fill is +/- 2-3% which is well within the 0.15% limits achieved by the MassMeter. The MassMeter, additionally, has no seals or moving parts exposed to the oils, so downtime and maintenance problems are minimised.

-  ENDS -

cgr/b/27.3.97